## Slide 1
ECE298A PROJECT PROPOSAL
TinyFIR
SPI-Programmable 8-Tap FIR Filter
A compact digital filter that stores the last eight samples and computes their weighted sum.
Hamza Soofi, Gurpal Johal, Mohil Kadakia and Ayaan Tunio
Notes: Hamza: We are proposing TinyFIR, an SPI-programmable eight-tap finite impulse response filter for a combined one-by-two Tiny Tapeout block on the GF180 process. A digital FIR filter computes a weighted sum of the current input sample and the seven samples before it to produce its generated output.
Mohil: Our design stores signed eight-bit samples and programmable coefficients. An external sample ready input controls when a new sample enters, so the sample rate can vary independently of the faster system clock. The key area decision is to use one multiplier and accumulator sequentially for all eight taps instead of building eight multipliers in parallel. That saves hardware area, while requiring several clock cycles for each output.
Hamza: The same hardware can demonstrate low-pass, high-pass and band-pass filtering by loading different coefficient sets through SPI. The chip is entirely digital, and any analog input conditioning or conversion happens outside the block.

## Slide 2
Filter architecture
One accepted sample triggers eight sequential tap calculations
Sample input
signed 8-bit
digital sample
Sample history
8 registers
shift on input ready signal
Tap selector
choose x[n−k]
and C[k]
Shared MAC
multiply + add
repeat for 8 taps
Scale + saturate
shift right 7
clamp to 8 bits
Output register
signed 8-bit
result + valid
SPI configuration
8 signed 9-bit coefficients
y[n] = Σₖ₌₀⁷ h[k]x[n−k]
Notes: Gurpal: This diagram shows the data path for one accepted sample. The eight-bit sample input feeds a bank of eight history registers. On an accepted sample ready input, the circuit stores the new sample and shifts the older values through the history. When the host sets the ready signal to high; it must keep the sample inputs stable through the cycle. The equation here shows that each sample is multiplied by a coefficient, then all eight products are added together.
Ayaan: The tap selector chooses one history sample and its matching coefficient. The SPI interface lets the host write those eight signed nine-bit coefficients. The controller then reuses one shared multiplier and accumulator: it multiplies the selected sample by its coefficient, adds the product, advances the tap index, and repeats until all eight taps are complete. This is the main area-saving decision in the architecture.
Gurpal: After the eighth tap, the accumulated fixed-point value shifts right by seven bits, then moves to the signed eight-bit output range. Saturation clamps an out-of-range result rather than allowing it to wrap around. The output register holds the result, and output_valid pulses for one system-clock cycle to announce that a new result is ready.

## Slide 3
Targets, verification & team
10 MHz
proposed system clock
≤16 cycles
processing latency target
500 ksample/s
maximum sample-rate target
Verification plan
Python integer reference model
Compare RTL against 10,000 random samples. Check reset, SPI writes, impulse response, unity pass-through, signed rounding, and saturation . Demonstrate low-pass, high-pass and band-pass responses.
Work split
Ayaan Tunio
FIR arithmetic datapath
Gurpal Johal
SPI and coefficient storage
Mohil Kadakia
Sample path, control and integration
Hamza Soofi
Python model and verification
Signed 8-bit samples / Signed9-bit coefficients / 20-bit Accumulator
GF180, 1 × 2 Tiny Tapeout block. Area and timing must pass the course implementation checks.
Eight taps support broad filter demonstrations; sharp frequency transitions are not promised.
Notes: Ayaan: These are proposed performance targets, not measured results. The design is planned for a 10 MHz system clock, and at most 16 cycles to finish calculating the sample output, and a maximum sample rate of 500,000 samples per second. At 10 MHz, that sample rate leaves twenty system-clock cycles between samples. The interface synchronization and processing both must fit the 20-cycle budget.
Hamza: For arithmetic, we use signed eight-bit samples, signed nine-bit coefficients stored as integers scaled by one hundred twenty-eight, and a twenty-bit accumulator. The output shifts right by seven and saturates to the signed eight-bit range. We will build the Python integer reference model and coordinate system verification. We plan to compare at least ten thousand random samples and check reset, SPI coefficient access, impulse response, pass-through, signed rounding, and variable-rate input.
Mohil: The final demonstrations will load coefficient sets for low-pass, high-pass and band-pass responses. Eight taps give relatively broad transitions, so we are not promising sharp frequency cutoffs. The work is divided by subsystem across Ayaan, Gurpal, Mohil and Hamza. All four members will review interfaces, help integrate the RTL and contribute to the results.